LED Street Light

Installation Instruction

# Summary

- The LED Street light is Eco-friendly& Energy-saving, and light source is high-power LED.

- Nice design, graceful shape; Moisture & heat resisted, tight-sealed.

- The housing is made of aluminum die-casting that can resist wallop and corrosion.

- Lens is designed according to street light standard with more scientific luminous distribution and higher luminous flux.

- Reasonable heat sink design can make sure light’s life span is longer than 30,000hours, and extremely low maintenance fee.

# Appearance Inspection

Before installation, please check the light carefully to see if all its parts are undamaged or fall-off in shipping &transportation, Inform original supplier if there is any damage.

# Application

Roads, streets, parking areas, bridges, highways, expressways, viaducts, intersections, crossroads, villas, campuses, hotel gardens, and docks etc.

# Technical Specification

| No. | Item | specification | Remark |
| --- | --- | --- | --- |
| Electrical Parameter | Power | 120W | classics |
|  | Input Voltage | AC90-260V |  |
|  | Power Connection | Y | Once production is damaged due to power connection, repair/replace by corresponding qualified technical staff |
| Optical Parameter | Lumens | 80lm/W |  |
|  | Color Temperature | 3500K-4000K |  |
|  | Color Rending Index | >70 |  |
| Working Condition | Operation Temperature | -25℃~45℃ |  |
|  | Operation Moisture | 10%-90% |  |
|  | Storage Temperature | ﹣40℃～80℃ |  |
|  | Moisture | 0-95%(No Condensation) |  |
|  | Protection Grade | IP65 |  |
| Others | Net Weight | 13.5Kgs |  |
|  | Dimension | 800*300*130mm（L*W*H） |  |
|  | Max. Projected Area | 0.04mm2 |  |
|  | Average Life | >30000 Hours |  |
|  | Light Sourcing | high power LED |  |
|  | LED | 90PCs |  |

# Installation：

Installation Option : Pole height : 8-9M, diameter of installation pole : 60mm

- 1. Connection Power cable: Brown cable connect the live wire of power supply, blue cable connect the neutral wire of power supply, the yellow and green cable connect the grounding wire. Connector place to be protected and fixed by PVC waterproof rubberized fabric.

- 2. Pole arm ② should be installed into installed fixer ③ and fixed by screws ④ (Screw by Torque: 8Nm), while keep street light parallel with the road surface

- 3. Connect electric power to start if everything is ready.

# Transportation and Storage

LED street lights are packaged by cartons. Severe mechanical shock, exposure and rain, upside down; throw, roll and stress are prohibited.

Lights should be stored in a dry and clean environment, the storage temperature is--20℃ to 45℃.

# Attention

1） Please connect positive wire and cathode correctly , otherwise lamp will be damaged

2） Please make sure the correct input voltage, otherwise lamp will be damaged.

3） Do not put those flammable objects like cloth, paper on the light when you are using, it should be better installed at a ventilated and good heat-dissipation place.

4)  To make sure light's good performance and longer life-span, abominable working ambient environment like mechanical shock, shake, sunshine direct radiation, salt mist and oil mist should be avoided when the light is working.

11. Security Caution

# We notice please follow the user manual's rules while using the product, those problems are not light's quality defect when you don't comply with the user's manual rules and lead to shorten the light's life-span or even cause damage on light.

# The company reserves the right to improve product and the final explanation right to product's specification.

FRX lighting Technology(Suzhou) Co.,Ltd.  Tel: 400-090-9893

# Text boxes

① Power Cable  ② Pole Arm

③ Installed fixer ④ Screw group